# Section XXXXX	Document & Manual Holders

- General

  - General

    - The Telecommunications Contractor shall supply and install documentation 	holders for proper display of all manuals, building drawings, disaster 	recovery and emergency procedure information.

    - The contractor is responsible to provide a complete turn-key installation based 	upon the specifications. All components shall be manufactured by 	Display-It of Toronto, Ontario (416) 699-5917

  - System Components

    - The document holders shall consist of the following key components

    - Wall Mount Flat Drawing Holder Features:

      - Clear wall mounted panel

      - PET G material construction

      - Mounting hardware to be supplied

      - Available in sizes to fit the appropriate drawing

      - Ability to replace drawings without removal from wall

    - Rack Mount Rolled Drawing Holder Features:

      - Clear rack mounted rolled drawing

      - Ability to hold multiple full size drawings

      - Hinged cover with polyprolene hinge

      - Supplied with key lock

      - PET G Material

      - Mounting hardware supplied

    - Wall Mount Manual Holder Features:

      - Clear wall mounted box

      - Supplied with key lock

      - PET G material

      - Mounting hardware supplied

      - Ability to hold 3” binder

    - Emergency Exit/Fire Exit Drawing Holder Features:

      - Red frame

      - Plexi glazing

      - Wall mountable

      - Secure wall mount hardware supplied

- Submittals

  - Submittals

    - Manufacturers’ Data: This literature shall include a description and technical data 	for all product supplied literature, should be as detailed as possible in the form of 	installation guides, datasheets, and user guides where applicable for all 	components.

    - Warranty information: All materials relating to warranties shall be included.

- Product

  - Acceptable Product

    - Wall Mount Flat Drawing Holders:

      - Display-It WH Series

      - Display-It SS Series

      - Display-It DS Series

      - Display-It SW Series

      - Display-It FH Series

    - Rack Mount Rolled Drawing Holders

      - Display-It TT Series

    - Wall Mount Manual Holders

      - Display-It MH Series

      - Display-it MP Series

    - Emergency Exit/Fire Exit Drawing Holders

      - Display-It ES Series

- Installation

  - Install all system components and appurtenances in accordance with the manufacturer's 	instructions, CSA, applicable Codes and as shown

    - Contractor shall verify:

      - Information presented in the Contract Drawings is correct.

Installation of equipment and work can be accomplished as indicated in 	the Contract Documents.

      - Contractor’s proposed product and methods of installation are 				compatible with 	existing conditions.
	
.

End of Section XXXXXX